Based on the MITRE ATT&CK framework, two data distributions can be defined: {D} rsub {tactic} , the distribution of techniques and tactics an arbitrary attacker would execute, and {D} rsub {system} , the behavioral distribution of regular system operations. {D} rsub {tactic} is represented by the Markov chain in figure 1, structuring valid transitions between the subset of MITRE ATT&CK tactics shown, such that this model could generate any valid sequence of attacker techniques. The parameters of this attacker behavior model could be determined empirically; instead, we defined all transitions on this model as uniformly distributed over valid transitions, which is a valid maximum-entropy model of attacker behavior in the absence of data. {D} rsub {system} is a model of regular system behavior described by monitoring data, including all cyber events: normal, outlier, anomalous, and attack events.
As a model of network activity, the high-dimensionality and temporal structure of {D} rsub {system} requires feature engineering, an open research topic. In this work, we represent {D} rsub {system} via a simple factorized conditional probability distribution {P} rsub {cpd} over hosts and network links for a variety of cyber event features: port usage, system event ids, flow volumes, and so forth. For example, the probability of two hosts communicating over port 80: p left (src =x.x.x.x , dest =y.y.y.y , port =80 right rline {D} rsub {system} , θ) , where θ represents one’s assumptions about how such a probability is structured. This feature could be defined as a Poisson distribution parameterized by the average rate of port 80 traffic between these hosts, or it might be defined by communication over port 80 given all other ports and their flow frequency for this directed pair of hosts, or even weighted ensembles of similar features. If properly structured, {P} rsub {cpd} can form an acyclic, directed Bayesian network. Such models are common in fields such as medical diagnoses [Warner, 2012] since they can be engineered and queried for to evaluate the probability of specific events; in our case, structured cyber events.
For our purposes, {P} rsub {cpd} simply provides a model for evaluating the local probability of MITRE ATT&CK tactic features at every host (node) and connection (edge) in the network, thereby assigning to each tactic its probability within regular system data. We assume, per the Unfetter Analytic platform, that every tactic {t} rsub {k} possesses a set of features {f} rsub {{t} rsub {k}} =\{ {f} rsub {event} , {f} rsub {netflow} , {f} rsub {pcap} , …\} , and {P} rsub {cpd} is constructed to provide a probabilistic representation by which to evaluate {p} rsub {cpd} ( {f } rsub {{t} rsub {k}} ) for every host and link. This value does not reflect the probability of the tactic within regular system behavior, but rather the probability of its observable features. Larger values are therefore detrimental since they represent system ‘camouflage’ surrounding a specific tactic’s behavioral features.

Methodology

As described, {D} rsub {tactic} models expected attacker actions, while {D} rsub {system} and {P} rsub {cpd} provide an empirical probabilistic model for observing specific events. Hidden Markov models (see Rabiner, 1989) provide a canonical view of these models, where {D} rsub {attack} represents the ‘hidden’ attacker transition model, and {P} rsub {cpd} models the emission probability of features over all host×tactic states. The distinction is that the structure and parameters of the hidden state model {D} rsub {attack} are assumed to form a uniform distribution over possible attacker actions.
Deriving an expectation over adversarial tactics on a system entails generating many attack sequences from {D} rsub {attack} and re-playing these on a system model {G} rsub {system} to track tactic frequencies. This gives an h×h×t frequency matrix {F} rsub {tactic} , whose entries left ({h} rsub {i} , {h} rsub {j} , {t} rsub {k} right ) represent the frequency of tactic {t} rsub {k} from host {h} rsub {i} to host {h} rsub {j} , where h is the number of hosts and t is the number of tactics. The diagonal elements of F represent on-host tactics, such as privilege escalation or execution, whereas off-diagonal elements represent transitional tactics involving two or more hosts, such as lateral movement or network discovery. The third tactic axis of this matrix simply preserves individual tactic frequencies. Overall, this simulation combines {D} rsub {attack} with actual system properties {G} rsub {system} to estimate the flow of attack information throughout the complete network.
Clearly for a fully-connected network (every host connecting to every host) and uniform random starting points, the tactic expectations derived from this simulation would simply converge to the stationary distribution of {D} rsub {attack} . However, the system properties of {G} rsub {system} impose structural conditions to validate tactic events according to link structure, whether or not a particular tactic is reasonable on a host, or other system knowledge. Hence, {G} rsub {system} imposes system-consistency constraints on walk generation, such that the output {F} rsub {tactic} approximates the distribution of {D} rsub {attack} conditioned to a specific network.
An expectation of tactic risk can then be calculated by evaluating {e} rsub {risk} left [i,j,k right ] = {P} rsub {cpd} left ({{f} rsub {t}} rsub {k} , {h} rsub {i} , {h} rsub {j} right ) * {F} rsub {tactic} [i,j,k] for all i, j, and k, giving {E} rsub {risk} , also of size h×h×t . {E} rsub {risk} represents the re-weighting of the system-wide tactic model {F} rsub {attack} by the local probability of observing behavioral features of tactics. Another view is that {E} rsub {risk} provides a model of the worst-case behavior of an attacker attempting to minimize his or her likelihood of detection, e.g., an optimal adversary.
By collapsing {E} rsub {risk} to an h×h matrix along its third (tactic) axis through summing, then rescaling every row by its sum, we derive a model of host vulnerability, {M} rsub {risk} . This model is conveniently a first-order Markov model lending itself to Markovian analyses (Winston, 1994). The utility of {M} rsub {risk} is that it integrates expected attacker behavior with the distribution of regular system behavior to derive a model of relative attack-risk; further, its construction incorporates the flow of information between all hosts, giving a system-wide measure of risk.
The stationary distribution of {M} rsub {risk} gives a well-defined metric of host-attack risk. From Markov chain theory, the distribution is calculated by repeated exponentiation, where {left ({M} rsub {risk} right )} ^ {k} = Π, as k→∞ . The resulting Π is an h×h matrix with identical rows left lbrace {π} rsub {0} = {π} rsub {1} =…= {π} rsub {h} =π right rbrace , π∈ {R} ^ {h} , for which the entries of π encode the stationary probability of attack features on a specific host, p left ({f} rsub {attack} , host= {h} rsub {i} right ) = {π} rsub {i} , where {π} rsub {i} denotes the ith element of π . Despite the asymptotic condition, convergence to π occurs rapidly for small k ; in this work k≤7 was sufficient. The full algorithm is shown in [figure 2].

Figure 2: Algorithm for the stationary attack-risk distribution of hosts.

Given the process for generating attack sequences from {D} rsub {attack} , and our empirically-derived probabilistic model {P} rsub {cpd} of observing attack features on or between hosts, the stationary distribution π represents a metric of host attack risk. Intuitively it represents how ‘normal’ attack features would appear on the network under regular conditions. This measure is informative in terms of determining high-risk hosts and links, and thereby optimizing sensor allocation or other attack mitigation strategies. Separate {π} rsub {{\{ t} rsub {k} \}} can also be evaluated for subsets of tactics \{ {t} rsub {k} \} , providing instead a measure of risk for specific tactics; this is done by selecting only the corresponding entries of {E} rsub {risk} along its third (tactic) axis when summing and normalizing this matrix to derive {M} rsub {risk} .

Experiments

Our simulated network consisted of devices simulating a complete substation: a SCADA windows host system, ABB COM600 automation controller, network firewall, and eight ABB REF615 protection relays, implementing ____ [baseline behavior?]. The monitoring system consisted of an open-source ELK stack tracking windows logs, netflows, Bro events, and Snort packet captures. Since Bro and Snort reflect more signature level detection schemes, in this project we only considered winlog and netflow data. The data lent a graphical model of the host-to-host communications per port, protocol, and flow size/timing, as well as the on-host events given by windows logs; this data model consisted solely of behavioral attributes and no signature-based features. The resulting graphical model consisted of host vertices and communication-based edges, each decorated with various embedded conditional distributions: p(eventId= {e} rsub {i} |host= {h} rsub {j} ) , p(port= {p} rsub {i} , src= {h} rsub {i} , dst= {h} rsub {j} ) , and so on. Therefore our probabilistic model {P} rsub {cpd} consisted of windows log events and netflows ____

Features of ATT&CK tactic techniques were manually defined based on known properties, where every technique (an instance of a tactic) had a list of ports and known windows log event ids by which to model their behavior. The majority of these properties blend in with common system events, but are expected to differ from the regular properties of our system data, {D} rsub {system} , which is generated from a highly regular industrial process. Various techniques’ features were defined for four core tactics: lateral movement, discovery, privilege escalation, and execution. The probability of observing a given tactic is then the union over all the features of all techniques included in that tactic. This foresees a weakness in our approach, which is that assessing tactic risk is dependent on the accuracy and precision of the features used to identify them; our assumption is that the highly regular system properties of an industrial network make common tactic features seem more obvious than a more open network.

Finally, using these systems and data models, we captured data over a complete month, in which all systems implemented their ordinary control logic. Amidst this data there were also several simulated attacks, one of which mirrored [Ukraine], in addition to relatively infrequent maintenance actions. Therefore, in addition to normal system noise and rare events, there were also signatures of real attacks and infrequent system maintenance tasks. Thus this dataset presented a real opportunity to test the method with realistic data which include high-frequency industrial activity, as well as noise (system and maintenance) and realistic attacks. As expected, the behavioral distribution for many features of interest resolved to long-tail distributions, such as the histogram of port usage between two given hosts.

Executing [TOMATO] we obtained the following results:

Host/device	p left ({f} rsub {attack} right rline host)
COM600, 192.168.2.10	0.3719
Relay 1, 192.168.2.101	0.114
Relay 2,192.168.2.102	0.1132
Relay 3, 192.168.2.103	0.0
Relay 4, 192.168.2.104	0.0253
Relay 5, 192.168.2.105	0.0
Relay 6, 192.168.2.106	0.0
Relay 7, 192.168.2.107	0.0
Relay 8, 192.168.2.108	0.1176
SCADA/HMI, 192.168.0.11	0.2579

Table 1: Host stationary attack-feature probability
As shown in [table 1], the high-centrality nodes 192.168.2.10 and 192.168.0.11 had the highest probability of attack feature observation, as expected both due to the higher complexity of their operations and their network centrality. The relays with zero probability reflect meters in normal operation, whereas for those with non-zero probability, we found that these values were attributable to actual attack events in the data, demonstrating the effectiveness of the approach. As such, the method provided a quantitative method by which to assess host vulnerability, readily identifying the high-risk, high-centrality nodes, but also identifying unusual behavior for end devices which we otherwise expected to implement highly regular and non-malicious event patterns. This means the method is useful both as a host-based risk-assessment tool, and as a detection method.

Commentary (Strengths and weaknesses)

The strength of the method is that the definition of features, and their associated probabilistic structure, is interpretable and well defined. This places an emphasis on feature engineering to build a proper and precise probability distribution sufficient to detect various attack tactics. Like signature detection, this outsources responsibility for feature creation to external sources; in contrast to signature detection, the method is capable of detecting unseen tactics since it is a behavior-based detection scheme, and hence detects attacks by class rather than by instance. A primary weakness is that these features also limit the scope of detection, such that if an attacker updates the features of their tactics to something undefined by the model of expected features, then their risk is no longer estimated. For example, an attacker executing an ssh-based tactic might configure ssh traffic to run over a common port like port 80, thereby evading any port-22 based statistical features registered for that tactic. Such extreme and advanced attacker behavior, where the distribution of tactic features obeys few regular properties, would only be detectable by means of anomaly/outlier detection or behavioral whitelisting. Ordinarily this is done by dimensionality reduction or clustering, by which the regular properties of

Rabiner, L. R. (1989). A tutorial on hidden Markov models and selected applications in speech recognition. Proceedings of the IEEE, 77(2), 257-286.

Winston, W. L. (1994). Operations Research. Algorithms and Applications.

Warner, H. R., Sorenson, D. K., & Bouhaddou, O. (2012). Knowledge engineering in health informatics. Springer Science & Business Media.

By simulating many attack sequences on the system model, one can assign to every host/edge a value for the probability of a specific tactic. These probabilities represent the probability of observing attack features via a model derived from normal system data, {D} rsub {system} , hence higher values represent higher risk, since a high tactic probability feature at some host translates as statistical ‘camouflage’ among normal system behavior.
Thus we can assign an empirical tactical probability to every host on the network, such that higher probabilities are undesirable, and likewise, hosts can be evaluated in comparative fashion in terms of which tactics to which they are most vulnerable. Via Markov network theory, this model can be collapsed into stationary host tactic probability distribution by …
The end result is a straightforward model of the stationary tactical risk at every node, given normal system behavior {D} rsub {system} and some attack feature model, f . We explicitly account for f , since only those tactics and techniques for which we define features will be detectable, and likewise these features must be updated over time as adversaries adapt and change their techniques. The benefit of this approach is that it lends a straightforward metric of relative risk within a system, and thereby offers a model toward the best allocation of sensors. Such Markovian systems are well-formed and interpretable, and also lend themselves to other analyses, such as evaluating the mean first-passage time that an adversary might be expected to spend at each host.

Feature-engineering to generate a high quality {P} rsub {cpd} need not be exceptionally complicated to model normal system behavior, since most cyber events can be simplified to categorical event frequency distributions; from these, one can derive more precise or complicated models simply by adding features. Often the probability of a specific event can be defined by the frequency of the event on the host(s) of interest, normalized by the frequency of all other events within that event class. However, such Bayesian models enjoy great flexibility in terms of the choice of distributions and the data by which to calculate them, allowing for the injection of domain knowledge.

As described previously, {D} rsub {attack} gives a Markovian model of attacker behavior embedding the actions an adversary could execute on a system, {D} rsub {system} contains all system data collected via a monitoring scheme, and {P} rsub {cpd} , derived from {D} rsub {system} , provides a model for evaluating the probability of ATT&CK tactic features, p( {f } rsub {tactic} ) .